## Slide 1: Agenda
Metrics
Test Results
Balance Results
Vissim

## Slide 2: Optimisation Performance
Empty network start, subcritical
Rolling start, subcritical
Empty network start, congested
Rolling start, congested
BUT FIRST, try sweeps for
Large Pop, Few Iter VS Small Pop, Many Iter
Random / Geometric / AverageTravelTimes
AlphaBuff mating rights

## Slide 3: Optimal Population Size: 60 vs 120
  Small Population
    Fast iterations
    Low diversity
            Large Population
    Longer iterations
    More diversity and more chances to improve by recombination
  For a cycle time of 120 s, using maximum bandwidth seed
  120 is the minimum number of individuals required to cover the whole search space
              At present, each evaluation takes about 1 s

## Slide 4: Optimal Population Size: 60 vs 120
  Results:
  The larger population performs better across the optimization
  BUT under time constraints the returns are not large enough to justify the extra computation time

## Slide 5: Population Seed Methods
  The population can be initialised by cloning the geometrical solution, offset by different values and slightly scrambled at the beginning, rather than starting off with completely random solutions.
  This improves the initial fitness and progress in the first few generations, but seems to also kill diversity and increase the chance of ending up in a local optimum.

## Slide 6: Balance Performance
One hour of Real-Time microsimulation
Balance-optimised timings ran on TRE
    No significant improvement overall
    Arc 6 better
On Equal Ground: ten minute window
Rolling start after 5 minutes “off”
    T = 0.12998771680873517
    S = 1.0317968397742057
    Q = 0.056581289833364037

## Slide 7: Balance Performance
  PROBLEM:
  the effects of the BALANCE optimization, when simulated in TRE, look awful:
    QUEUES rapidly get out of control
    SPILLBACK occurs and fills entire arcs.
  The optimization looks pretty effective in Vissim.
What can be the source of discrepancy?
Effective green should be better modelled by Vissim, since in microsimulation vehicles have finite acceleration, so if anything the saturation flows should be even higher.
Timing may be an issue, if flows are expected later because of more realistic acceleration, in TRE they will reach the next junction during the red phase and stop. See next slide.
Calibration of the models?

## Slide 8: Balance Performance
  HYPOTHESIS: Different acceleration modelling between micro-and macrosimulation causes Vissim based synchronization to fail in TRE.
If this was the case I would expect to find similar offset patterns between the TRE based and Balance optimisations, with the latter showing slightly longer relative offsets between subsequent junctions.

## Slide 9: Optimal Population Size
First text layer for running text in 14pt
  Second level layer for Headlines in 18pt
    Third level layer for bullet points in 14pt
      Fourth level layer for bullet points 14pt
        Fifth level for numberings 14pt
          Sixth level for numberings 14pt
            Seventh level for Key Message
              Eighth level for Key Message
                Ninth text layer for caption, footnotes 8pt
  Information
To change from one text layer to the next, use the Increase / Decrease List Level buttons:
Or with your keyboard: ALT+SHIFT+LEFT or RIGHT

## Slide 10: Information
  Drawing guides
You can enable your guidelines to align objects on the slide.
Hit the right mouse button outside the slide and go at „Grid and Guides…“
  Slide layouts
You can choose between different slide layouts.
Click on the Home-tab | New Slide or Layout | and choose one out of the layouts.
  Footer
You can insert or change your presentation‘s footer. Click on the Insert-tab | Header and Footer.
Deactivate Date and Time.

## Slide 11
CONTENT
HEADLINE & LOGO
FOOTER / LOGO